## Slide 1: CSC3050 – Computer Architecture
Quiz 2 (group competition)

## Slide 2
Example
What is the universally adopted standard for floating-point numbers?
ACM 754
IEEE 754
ANSI 754
ISO 754
Answer: 2

## Slide 3
Are you ready ?

## Slide 4
1) Which standards have been widely adopted in the field of floating-point arithmetic?
IEEE 754-1985 for single-precision and double-precision floating point numbers
IEEE 754-2008 for quad-precision and half-precision
IEEE 754-2024 for mini-float (FP8) and FP4
IEEE 754-2008 for bfloat16 and FP16
Answer: 1,2

## Slide 5
2) What is the value of the following hexadecimal number?
80000000
1.0
NaN
-0.0
-2.0
0.0
Answer: 3

## Slide 6
3) Which decimal numbers have exact representations in IEEE 754 FP format?
0.1
0.2
0.3
0.5
0.0625
Answer: 4,5
Notes: binary system can only represent fractions that are sums of negative powers of 2 (e.g., 1/2, 1/4, 1/8, etc.).

## Slide 7
4) What are denormalized numbers?
Floating-point numbers that are too small to fit in the standard format
Floating-point numbers that are too large to fit in the standard format
Floating point numbers that are not yet normalized
Denormalized numbers have an exponent of 0, and the hidden 1 in the significand is excluded.
Answer: 1,4

## Slide 8
5) In Project #3, we have assumed a fast integer multiplier where many parallel adders are used, and each adder computes a partial product. Then, all the partial products are combined to yield a single result. The shape of the organization of those adders earns a special name, which is:
The Prism
The Pagoda
The Pyramid
The Palace
The Paragon
Answer: 3

## Slide 9
6) In Project #3, which RISC-V model are you constructing?
RV64I
RV32IM
RV32IF
RV32G
Answer: 2

## Slide 10
7) Why does FMAC (Fused Multiply and Accumulate) provide more accurate results than a separate Fmul and Fadd sequence?
Separate FMUL and FADD would require two roundings, FMAC requires only one
Separate FMUL and FADD would require two normalizations, FMAC requires only one
FMUL and FADD have data dependencies, resulting in a loss of precision.
Merged operations are always more accurate
Answer: 1

## Slide 11
8) Nvidia Blackwell supports FP4 format in AI applications. What benefits does the FP4 format provide?
FP4 could double the computational throughput compared to FP8.
FP4 leads to improved power efficiency
FP4 results in more accurate predictions for AI applications
FP4 reduces the memory bandwidth requirements to load/store model parameters and activations
Answer: 1,2,4
Notes: GCC has extensions to use BFloat16 format

## Slide 12
9) What do x86 SIMD, RISC-V Vector, and Nvidia GPUs have in common?
They all support DLP (Data Level Parallelism)
They all perform the same operation on multiple data elements.
They all originated from the graphics processing paradigm
They are all suitable for control-intensive tasks
They all require high memory bandwidth
Answer: 1,2,5
Notes: GCC has extensions to use BFloat16 format

## Slide 13
10) Compared to a pipelined data path, a single-cycle data path typically has:
  1) Higher throughput
  2) Faster clock rate
  3) More complex control logic
  4) A longer operation latency
  5) A lower CPI
Answer: 5

## Slide 14
11) Which of the following statements about single-cycle data path implementation is true?
CPI is 1, every instruction must finish in one cycle
The clock cycle must accommodate the slowest instruction
The resources in the data path cannot be reused in the same cycle
The result is written back to the register file in the same clock cycle.
Answer: 1,2,3

## Slide 15
12) What hazards will decrease the efficiency of a pipeline?
  1) Structure hazards
  2) Data hazards
  3) Instruction hazards
  4) Forward hazards
  5) Control hazards
Answer: 1,2,5

## Slide 16
13) Which of the following implementations may have a CPI lower than 1?
Single-cycle data path implementation
Multi-cycle data path implementation
Pipelined implementation
Superscalar implementation
Answer: 4

## Slide 17
14) What are the key principles of designing a pipelined data path?
  1) Multi-stage execution
  2) Increased throughput
  3) Overlapped execution
  4) Lowered instruction latency
  5) Improved resource utilization
Answer: 1,2,3,5

## Slide 18
15) What might occur if we double the number of pipelined stages from 5 to 10?
  1) The clock rate might become faster
  2) The branch misprediction penalty becomes higher
  3) The data hazard penalty might increase
  4) The throughput is likely to increase
  5) More pipelined registers are required
Answer: 1,2,3,4,5

## Slide 19
16) What (HW/SW) strategies can reduce pipeline stalls caused by data hazards?
  1) Increase the pipeline stages
  2) Data forwarding
  3) Adding multiple functional units
  4) Compiler instruction scheduling
  5) Branch prediction
Answer: 2,4

## Slide 20
17) Branch prediction should be performed at which of the pipelined stage?
1) WB
2) ID
3) EXE
4) IF
5) MEM
Answer: 4

## Slide 21
18) Which of the following are considered part of “architecture states”?
The BHT
The BTB
The general purpose registers
The PC
The pipelined registers
Answer: 3,4

## Slide 22
19) CPU Time = Inst count X CPI X Clock cycle time
SIMD/Vector instructions can significantly reduce Inst count
Pipeline processors reduce Clock cycle time
Multi-cycle data paths reduce Clock cycle time
Superscalar processors reduce CPI
Adding Fused-Mul-Add (fma) instruction reduces all three parameters.
Answer: 1,2,3,4

## Slide 23
20) Frequent stalls in the pipeline are likely to occur when traversing a linked list in a loop because of:
Structure hazards
Date hazards
Data hazards
Control hazards
Answer: 3

## Slide 24
21) Which integer adder can provide a one-cycle latency?
A Ripple-carry adder
1’s complement adder
A Carry-Lookahead (CLA) adder
A Quantum adder
Answer: 3

## Slide 25
22) Which of the following could be effective for static branch predictions?
Predict a backward branch taken
Predict a forward branch not taken
Predict the beq rs1, x0 not taken
Predict the blt instructions taken
Answer: 1,2,3

## Slide 26
23) Which of the following are NOT techniques used to address control hazards?
  1) Pipeline stalls
  2) BTB (Branch Target Buffer)
  3) Branch prediction
4) Data forwarding
Answer: 4

## Slide 27
24) What type of parallelism is exploited by the compiler code scheduling?
  1) DLP
  2) TLP
  3) ILP
4) MLP
Answer: 3

## Slide 28
Section II
(2 points per question)

## Slide 29
25) What information is used to index a branch prediction table in correlated branch prediction (also known as 2-level adaptive branch prediction)?
PC
Branch target address
Top of the return address stack
Global branch history
Answer: 1,4
Notes: RISC-V has no opcode as 0000000 (illegal instruction)

## Slide 30
26) A 32-bit memory word consisting entirely of 1’s; what could it mean?
Signed integer value -1
Unsigned integer 231-1
Single precision FP value -1.0
It is a NaN in single precision FP format
It is a pointer to the highest address within the 4GB memory space.
Answer: 1,4,5
Notes: RISC-V has no opcode as 0000000 (illegal instruction)

## Slide 31
27) A 32-bit memory word containing all 0s; what could it mean?
Signed integer value 0
Single precision FP value 0.0
It is a denormalized number (exponent is 0)
It is a NULL pointer
It is a NOP instruction on the RISC-V processor
Answer: 1,2,4
Notes: RISC-V has no opcode as 0000000 (illegal instruction)

## Slide 32
28) Saturation arithmetic is particularly useful and often necessary for which data types?
  1) Floating point data
  2) Audio processing
  3) Video processing
  4) Quantized data in AI models (e.g. int4, int8)
  5) Text data
Answer: 2,3,4

## Slide 33
29) In our RV32I pipelined data path, which stage requires two adders?
  1) ID
  2) IF
  3) EXE
  4) MEM
  5) WB
Answer: 3

## Slide 34
30) Which implementations are not suitable for vanilla Von Neumann architecture?
  1) A Single Cycle Data Path
  2) A Multi-cycle Data Path
  3) A Pipelined Data Path
  4) A Superscalar Data Path
Answer: 1,3,4

## Slide 35
31) What are the advantages of untagged BHT (Branch History Table)?
Simple
Fast
Consume less energy
Good for high-performance microprocessors
Low cost
Answer: 1,2,3,5
Notes: Quad-precision, FP16, and Bfloat16

## Slide 36
32) Which of the following control signals must be propagated through the pipelined registers to the WB stage?
Rd (target register)
WRen (write-enable)
WBsel (Write back selection)
BReq
Answer: 1,2,3

## Slide 37
33) RISC-V has a fixed instruction length (assuming NO C extension), a highly regular instruction format, and simple instructions. So RISC-V is more suitable for which of the following implementations?
Single cycle implementation
Multi-cycle implementation
Pipelined implementation
Super-scalar implementation
Answer: 1,3,4

## Slide 38
34) A basic block has 50 instructions; how many legal schedules are possible?
In the best case, 1 schedule only
50
In the worst case, 50! possible schedules
Less than 50x50
Answer: 1,3
Notes: RISC-V has no opcode as 0000000 (illegal instruction)

## Slide 39
35) A compiler can reorder instructions to prevent data hazards. Nonetheless, the compiler often faces limitations due to what constraints?
  1) Scheduling are error prone
  2) Memory dependencies may not be known due to possible memory aliasing
  3) The scope of scheduling is limited due to frequent branches
  4) Users do not want to pay for compiler optimizations
Answer: 2,3

## Slide 40
36) When running a binary tree search on a pipelined data path, what hazards are likely to occur?
  1) Tree hazards
  2) Structure hazards
  3) Data hazards
  4) Control hazards
  5) Divergence hazards
Answer: 3,4

## Slide 41
37) Why do some RV pipelined data path designs utilize a comparison unit to execute the branch-and-compare instead of using the standard ALU?
The comparison unit could be faster than subtraction
Avoid setting the wrong ‘taken/not-taken’ control signal due to subtraction overflows.
The ALU at the EXE stage is needed for R-type instructions and Load/Store instructions
Comparison operation does not trap
Answer: 1,2,3