## Slide 1: CSC3060 – Computer Systems
Review Pop Quiz

## Slide 2
Section I
(single answer)
For students who have not received >2 points before

## Slide 3
In computer architecture, the term “memory wall” refers to which of the following?
The gap between the disk and the memory
The gap between DRAM and SRAM
The gap between the registers and the L1 data cache
The gap between CPU and the main memory (DRAM)
Answer: 4

## Slide 4
2) Which of the following pieces of information is not stored as part of a data cache line?
Data of the cache block
Set number
The valid bit
The address tag
The dirty bit
Answer: 2

## Slide 5
3) In a memory hierarchy, which layer is managed by the compiler or the programmers?
The local memory
The L1 cache
The L2 cache
The write buffer
Answer: 1

## Slide 6
4) We have a 64 KB, 4-way set-associative cache with a 32-byte block (line) size. When the CPU issues a 32-bit memory address, how many bits are allocated to the Tag, the Set Index, and the Block Offset, respectively?
16, 11, 5
18, 8, 6
18, 9, 5
17, 9, 6
Answer: 3

## Slide 7
5) Which of the following data structures is used in a non-blocking cache?
A prefetch buffer
AMAT counter
MSHR
Interlock table
Answer: 3

## Slide 8
6) Which of the following cache organizations does not make sense?
L3 is write-through
L1 is direct-mapped plus a victim cache
L2 write-back with write allocate
Split L1I / L1D
Answer: 1

## Slide 9
7) In a typical modern multi-core processor, which level of cache is usually shared among all the CPU cores?
1) L1
2) L2
3) L3
4) L4
Answer: 3

## Slide 10
8) For a single-cycle data path design, if the D-cache miss rate is 5%, 40% of instructions are load/stores, and the memory latency is 100 cycles. What would be the average CPI?
  2.0
  1.4
  1.6
  3.0
Answer: 4

## Slide 11
9) The instruction cache is usually easier to manage than the data cache. Why?
It does not need to handle write operations
It does not need the valid bit
It does not need to handle cache line replacements
It does not need the tag bits
Answer: 1
Notes: RISC-V has no opcode as 0000000 (illegal instruction)

## Slide 12
10) In modern processors, what is the likely L1D cache hit latency?
1 cycle
3-4 cycles
5-6 cycles
10+ cycles
Answer: 2
Notes: RISC-V has no opcode as 0000000 (illegal instruction)

## Slide 13
Section II
(multiple answers)

## Slide 14
11) What is the most likely cache organization for L1D in modern processors?
4-way set-associative, write-through, write-allocate,
Fully-associative, write-through, write-noallocate,
Direct-mapped, write-back, write-allocate,
4-way set-associative, write-back, write-allocate,
Direct-mapped, write-back, write-noallocate,
Answer: 4
Notes: RISC-V has no opcode as 0000000 (illegal instruction)

## Slide 15
12) If minimizing the tag space is the primary goal, which cache features should be used?
Set associative caches
Direct-mapped caches
Write no-allocate policy
Large cache blocks (lines)
Inclusive caches
Answer: 2, 4

## Slide 16
13) Modern processors typically include on-chip L1, L2, and L3 caches. Which statement is TRUE?
1) The primary goal of L3 cache is to reduce the memory traffic to the memory
2) The primary goal of the L1 cache is to have a fast hit time
3) The L3 cache is often shared by multiple cores
4) The L2’s goal is to balance the speed and the capacity
Answer: 1,2,3,4

## Slide 17
14) What are the four types of cache misses (4C’s) ?
Compulsory misses, Conflict misses, Capacity misses, Coherence misses
Cold misses, Collision misses, Capacity misses, Coherence misses
Cascaded misses, Controlled misses, Contiguous misses, Conditional misses
Cool misses, Cold misses, Capacity misses, Coherence misses
Answer: 1,2

## Slide 18
15) Among the 4C’s, which cache misses are the most difficult to remove?
Compulsory
Collision
Capacity
Coherence
Answer: 4

## Slide 19
16) For the compulsory misses, how may we reduce them?
Hardware prefetching
Having a larger cache line size
Increase the cache size
Add a victim cache
Answer: 1,2

## Slide 20
17) Compare the L2 to the L1 cache, the L2 cache is usually
Larger
Slower
Unified
Shared
Answer: 1,2,3

## Slide 21
18) Four processors are connected to the main memory via a global bus. What are the possible solutions to maintain cache coherence?
Use a shared cache; no private cache allowed
If caches are private, use the Snoopy protocol
Build an inclusive multi-level cache
Split the instruction and the data cache
Answer: 1,2

## Slide 22
19) Assume the same cache size and the same line size. Which of the following statements are always true?
A direct-mapped cache is faster than set associative caches
A fully associative cache has the lowest cache miss rate
A direct-mapped cache has the lowest tag overhead
Replacement policy in a direct-mapped cache is the simplest
Answer: 3,4

## Slide 23
20) What are the advantages of using a large cache line size?
It exploits more spatial locality
It exploits more temporal locality
It saves tag space
It could reduce compulsory misses
Answer: 1,3,4

## Slide 24
21) My computer has a two-way set associative cache with 4KB and 32B line size, which of the following memory reference sequences would run into conflict misses?
1) 0x01ABC000, 0x01ABC004, 0x01ABC010, 0x01ABC002,
2) 0x01ABC000, 0x01ABC020, 0x01ABC030, 0x01ABC040,
3) 0x01ABC000, 0x01ABB004, 0x01ABD000, 0x01ABA010,
4) 0x01ABC020, 0x01ABC030, 0x01ABC02A, 0x01ABC03A,
Answer: 3

## Slide 25
22) What is the multi-level cache implemented in your project #4?
Inclusive cache
Exclusive cache
NINE cache
Shared cache
Answer: 3

## Slide 26
23) What replacement algorithm is implemented in the typical set-associative caches today?
LRU
FIFO
Approximate LRU
Random
Belady’s algorithm
Answer: 3

## Slide 27
24) If you would like to implement a TRUE LRU replacement algorithm, what data structure should be used?
A queue
A stack
A tree
A heap
Answer: 2

## Slide 28
25) You developed a new cache replacement algorithm that effectively balances procedure calls and looping behaviors. Now, what is the upper bound you need to evaluate against?
Against LRU
Against Random
Against Belady’s algorithm
Against a perfect cache
Answer: 3

## Slide 29
26) My cache supports both write-allocate and write-no-allocate policies; it is controlled by a bit in the store instruction. Under what condition should the store instruction turn on “write-no-allocate”?
In the memcpy(a,b,n) lib call when n is large
When storing local variables in a procedure
When storing a struct member (e.g., st.a or st->a)
In the memset(a,b,n) lib call when n is large.
When writing database logs
Answer: 1,4,5

## Slide 30
27) Which cache features require greater bus and memory bandwidth?
Large cache lines
Cache prefetching
Non-blocking caches
Exclusive, multi-level, write-back caches
Write-through caches
Answer: 1,2,3,5

## Slide 31
28) Which of the following statements about the “snoopy” cache are true?
It works as a watchdog for preventing illegal cache references
It is designed to maintain cache coherence for bus-connected multi-processor systems
It is designed for data security enforcement
It will generate significant snooping bus traffic
Answer: 2,4

## Slide 32
29) Which of the following could reduce conflict misses incurred in a direct-mapped L1D cache?
Increase the cache sizes
Increase the cache block (line) sizes
Add a victim cache
Change to set associative cache
Use the best replacement algorithm
Answer: 1,3,4

## Slide 33
30) Which of the following are often useful in reducing cache capacity misses?
Increase the cache sizes
Increase the cache block (line) sizes
Add one victim cache
Change to set associative cache
Cache prefetching
Answer: 1,5

## Slide 34
31) MSHR (Miss Status Handling Registers) are used to track multiple outstanding cache misses. Each level of cache has its own MSHR. On a multicore chip, the number of entries in the L3 MSHR would likely be influenced by
The memory latency
The memory bus width
The size of the L2 cache
The number of cores sharing the L3
Answer: 1,2

## Slide 35
32) I-cache does not take stores from the processor. However, modern applications use “instruction patching” or “JIT” code generation to either modify instructions or generate a new code section for subsequent execution. Which of the following solutions are required for evicting stale instructions in the I-cache?
Flush the I-cache to purge all old instructions
Invalidate the I-cache lines containing the instructions
Flush the data caches
Maintain coherence between I- and D-cache: any updates to the D-cache will also write into the respective lines in I-cache.
Answer: 1,2,4

## Slide 36
33) Which of the following multi-level cache organizations does not make sense?
L1I copy back and L1D write-through
L1/L2 exclusive, L2/L3 inclusive
L1D 4-way set associative, L2 direct mapped
L1/L2 inclusive, L2/L3 exclusive
Answer: 1,2,3

## Slide 37
34) In contemporary processors, the vast majority of chip space is dedicated to what?
Branch prediction
Register files
Pipelined registers
Floating-point functional units
Caches
Answer: 5

## Slide 38
35) Which of the following sorting algorithms is known to have high data locality?
Quicksort
Insertion sort
Heapsort
Radix sort
Bubble sort
Answer: 1,2,5

## Slide 39
36) What is the difference between a hardware cache and a software cache (such as a disk file cache)?
Software caches are managed by system software or applications, whereas hardware caches are managed by the hardware
Hardware caches support associative search, while software caches utilize lookup data structures such as hash tables.
Hardware caches must implement simple and fast replacement algorithms; software caches can use more complex algorithms.
Hardware caches are flexible in size, but software caches are not.
Answer: 1,2,3